## Slide 1
FINAL YEAR PROJECT REVIEW — PHASE I (ACADEMIC YEAR 2026–2027)
Confidence-Driven Probabilistic Machine Learning Framework for Electricity Demand–Supply Gap Forecasting and RAG-Based Energy Planning
STUDENT PRESENTERS
• S. Udayakumar (43120227)
Role: Model Architecture & Time-Series Engineering
• D. Tamilarasu (43120224)
Role: Uncertainty Estimation & Gap Analytics
• Suganth Kesavan (43120216)
Role: RAG Pipeline & Decision Support System
PROJECT SUPERVISOR & INSTITUTION
Project Supervisor: Dr. Kamatchi K. S
Academic Designation: Associate Professor
Department: Department of Information Technology
Focus Area: Energy Analytics, Deep Learning & Applied AI
Academic Year: 2026 – 2027 (Final Year Engineering Project)

## Slide 2
FINAL YEAR PROJECT REVIEW — PHASE I
Presentation Agenda & Review Structure
02
Department of Information Technology | Confidence-Driven Probabilistic ML & RAG Energy Planning Framework
01
Introduction & Background
Electricity demand growth, renewable intermittency, and the balancing dilemma.
02
Problem Statement & Gaps
Identified limitations in isolated forecasting and unquantified prediction uncertainty.
03
Aim, Objectives & Scope
Project goals, 7 specific technical objectives, and Tamil Nadu grid scope.
04
Expected Technical Outcomes
Dual forecasting, 90/95/99% PIs, gap quantification, and RAG energy planning.
05
Literature Survey
Analysis of 5 major benchmark papers with methodology and limitation mapping.
06
Research Gap Analysis
Structured comparative matrix contrasting conventional approaches with our framework.
07
Feasibility & Risk Assessment
Technical, economic, operational, and environmental feasibility with risk matrix.
08
System Architecture & Flow
Decoupled dual-stream forecasting architecture and RAG knowledge retrieval pipeline.
09
Materials, Methods & Data Analysis
Datasets, feature engineering, ML algorithms, and statistical uncertainty formulation.
10
Validation, Timeline & Future Work
Jan–Mar 2026 test benchmark, model performance metrics, Gantt chart, and Phase II plan.

## Slide 3
FINAL YEAR PROJECT REVIEW — PHASE I
Introduction & Background: Power Grid Dynamics
03
Department of Information Technology | Confidence-Driven Probabilistic ML & RAG Energy Planning Framework
1. Rising Electricity Demand & Urbanization
• Rapid economic expansion, EV adoption, industrial automation, and digital infrastructure drive steep surges in power demand.
• Peak load swings exhibit sharp seasonal variations and extreme non-linear intraday fluctuations.
2. Renewable Integration & Intermittency
• Accelerated transition towards carbon neutrality via massive integration of Solar PV and Wind energy systems.
• Generation is strictly weather-dependent (solar irradiance, wind velocity, ambient temperature, monsoon precipitation).
3. The Demand–Supply Balancing Dilemma
• Severe operational challenge in maintaining instantaneous generation-load equilibrium at State Load Despatch Centres (SLDC).
• Unsynchronized demand surges and generation drop-offs cause acute grid frequency deviations and reserve strain.
4. Paradigm Shift: Uncertainty & RAG Planning
• Conventional point forecasts fail to provide operational confidence margins or risk boundaries for spinning reserves.
• Critical need for probabilistic prediction intervals (90%, 95%, 99%) coupled with knowledge-grounded RAG energy planning.
Key Insight: Safe grid planning requires simultaneous demand-supply gap forecasting, multi-level confidence bounds, and actionable policy guidance.

## Slide 4
FINAL YEAR PROJECT REVIEW — PHASE I
Problem Statement: Key Limitations in Existing Systems
04
Department of Information Technology | Confidence-Driven Probabilistic ML & RAG Energy Planning Framework
Problem 1: Isolated & Siloed Forecasting
• Existing literature overwhelmingly treats electricity demand and renewable supply as separate problems.
• Failing to model both dimensions simultaneously prevents grid planners from knowing the net imbalance in advance.
Problem 2: Deterministic Point Prediction Deficits
• Standard ML/DL systems produce single deterministic values (point forecasts) without confidence bounds.
• Point predictions fail to communicate forecast uncertainty, leaving operators blind to tail-risk extreme scenarios.
Problem 3: Absence of Integrated Gap Forecasting
• Direct mathematical gap forecasting with combined uncertainty quantification is practically non-existent in state grids.
• Without a synchronized gap model, reserve capacity allocation is either over-provisioned (wasteful) or under-provisioned (outages).
Problem 4: Disconnect from Actionable Energy Planning
• Existing forecasting algorithms output raw numbers and terminate without contextualized operational guidance.
• Grid operators lack automated, policy-grounded decision support to translate numerical shortages into concrete actions.
CORE RESEARCH OBJECTIVE ADDRESSED:
To bridge this gap by designing an end-to-end framework integrating: (1) Decoupled Demand and Supply ML Forecasting, (2) Probabilistic Uncertainty & Prediction Intervals (90%, 95%, 99%), (3) Demand–Supply Gap Quantification, and (4) RAG-based Energy Planning Recommendations.

## Slide 5
FINAL YEAR PROJECT REVIEW — PHASE I
Project Aim, Key Objectives & Operational Scope
05
Department of Information Technology | Confidence-Driven Probabilistic ML & RAG Energy Planning Framework
PROJECT AIM
To develop a confidence-driven probabilistic machine learning framework that forecasts electricity demand and source-wise supply, quantifies prediction uncertainty through multi-level prediction intervals, estimates the future demand–supply gap, and provides knowledge-grounded energy planning recommendations via Retrieval-Augmented Generation (RAG).
PROJECT SCOPE & BOUNDARIES
• Geographical Focus: Tamil Nadu Power System & State Load Despatch Centre (SLDC).
• Temporal Scope: 129 monthly observations (April 2015 – December 2025).
• Forecast Horizon: 3-month forward operational planning window (Jan–Mar 2026).
• Supply Sources (8): Coal, Oil & Gas, Nuclear, Hydro, Solar, Wind, Small Hydro, Bio-Power.
• Meteorological Data: Temperature, Relative Humidity, Rainfall, Solar Irradiance.
SPECIFIC TECHNICAL OBJECTIVES
1. Demand Forecasting: Develop ML/DL models (RF, XGBoost, LightGBM, LSTM) to forecast monthly electricity demand using lag and weather features.
2. Supply Forecasting: Train independent ML/DL models to forecast monthly source-wise power generation across thermal, nuclear, and renewable sources.
3. Uncertainty Quantification: Estimate prediction uncertainty using the historical validation residual distribution (standard error sigma).
4. Multi-Level Prediction Intervals: Construct 90%, 95%, and 99% symmetric confidence bounds around point forecasts using standard normal critical values.
5. Demand–Supply Gap Analysis: Calculate the net operational gap (Gap = Predicted Demand - Predicted Supply) and combine standard errors (sigma_G = sqrt(sigma_D^2 + sigma_S^2)).
6. Risk & Condition Classification: Perform deterministic threshold classification (Shortage/Surplus/Balanced; Low <3000 MU, Moderate 3000-4500 MU, High >4500 MU).
7. RAG Knowledge Planning: Retrieve trusted energy policies, grid regulations, and CEA guidelines from a FAISS vector database to generate LLM-powered planning advice.

## Slide 6
FINAL YEAR PROJECT REVIEW — PHASE I
Expected Technical Outcomes & System Deliverables
06
Department of Information Technology | Confidence-Driven Probabilistic ML & RAG Energy Planning Framework
1. Accurate Demand Forecasting Engine
• High-accuracy monthly demand point forecasts.
• LSTM outperforms baselines with R² = 0.78, MAE = 368.72 MU, MAPE = 3.41%.
2. Source-Wise Supply Forecasting Engine
• Independent forecasting of 8 energy generation sources.
• LSTM captures renewable intermittency with R² = 0.56, MAE = 731.56 MU, MAPE = 6.30%.
3. Multi-Level Prediction Intervals
• Quantified uncertainty with 90%, 95%, and 99% confidence bands.
• Provides grid operators with rigorous statistical boundaries for tail-risk planning.
4. Mathematical Demand–Supply Gap Estimation
• Direct quantification of net state electricity deficit/surplus.
• Propagated standard error: sigma_G = sqrt(sigma_D^2 + sigma_S^2) = 1,070.88 MU.
5. Deterministic Risk & Threshold Classification
• Clear operational condition status: Shortage, Balanced, or Surplus.
• Threshold severity bands: Low (<3000 MU), Moderate (3000–4500 MU), High (>4500 MU).
6. RAG-Powered Energy Planning Advice
• Knowledge-grounded recommendations synthesized by LLM.
• Grounded in CEA, TNERC regulations, spinning reserves, and demand response protocols.

## Slide 7
FINAL YEAR PROJECT REVIEW — PHASE I
Literature Survey: Summary of Key Benchmark Studies
07
Department of Information Technology | Confidence-Driven Probabilistic ML & RAG Energy Planning Framework
Author / Year | Method / Model | Application Domain | Major Finding | Identified Limitation
Chisale et al. (2025) [5] | ECEEMDAN-BiGRU & Quantile Regression | Electricity Demand Forecasting | Signal decomposition effectively extracts non-linear trends; quantile regression yields robust demand intervals. | Focuses exclusively on demand; completely omits supply-side forecasting & gap estimation.
Cao et al. (2022) [15] | Transformer-Guided State Space (TPEDF) | Probabilistic Demand Forecasting | Transformer attention captures long-term dependencies while state-space model quantifies uncertainty distributions. | Single-side forecasting; lacks demand-supply integration and actionable decision support.
Terrón-Serrano et al. (2026) [13] | Shared Probabilistic Distributions | Day-Ahead Demand & Renewables | Joint probabilistic modeling of load and renewables using weather data improves reserve scheduling efficiency. | Does not compute operational gap intervals or incorporate RAG-based regulatory planning.
Ni et al. (2024) [16] | ChatGrid: LLM + RAG Pipeline | Power Dispatching Knowledge Q&A | Retrieval-Augmented Generation grounds LLM answers in grid dispatch rules, dramatically cutting hallucinations. | Standalone conversational Q&A system; lacks integration with numerical ML forecasting engines.
Debnath et al. (2025) [29] | Weather-Informed LSTM & Transformer | Extreme Weather Grid Load Forecasting | Incorporating multi-source weather variables (temperature, humidity) significantly reduces peak load forecast errors. | Deterministic point predictions only; no confidence intervals or supply-gap risk assessment.

## Slide 8
FINAL YEAR PROJECT REVIEW — PHASE I
Research Gap Analysis: Conventional vs Proposed Framework
08
Department of Information Technology | Confidence-Driven Probabilistic ML & RAG Energy Planning Framework
Evaluation Dimension | Existing Approaches | Proposed Framework | Research Gap Addressed
Forecasting Scope | Forecasts demand or supply in isolation (siloed models) | Decoupled, synchronized dual-stream forecasting (Demand + Supply) | Eliminates operational mismatch between generation and load
Prediction Nature | Deterministic point forecasts (single values) | Confidence-driven probabilistic forecasting with multi-level bounds | Quantifies prediction uncertainty for tail-risk management
Prediction Intervals | Rarely implemented, or single-level (e.g., 95% only) | Multi-level 90%, 95%, and 99% symmetric prediction intervals | Offers customizable risk tolerance margins for SLDC operators
Demand–Supply Gap | Heuristic or post-hoc comparison without uncertainty | Dedicated mathematical gap engine with combined sigma_G propagation | Provides rigorous statistical confidence bounds for net deficit/surplus
Risk Assessment | Manual, ad-hoc threshold inspection by engineers | Deterministic 3-tier severity classification (Low, Moderate, High) | Standardizes automated dispatch alerts and operational priority
Energy Planning | Disconnected static rulebooks or ungrounded LLMs | Integrated RAG engine with FAISS vector retrieval & grounded LLM | Bridges numerical forecast outputs directly to policy-grounded actions
Key Innovation Summary:
Our framework uniquely closes the loop: Data Ingestion -> Decoupled ML Forecasting -> Multi-Level Residual Uncertainty -> Mathematical Gap Estimation -> Deterministic Risk Classification -> RAG-Grounded Energy Planning.

## Slide 9
FINAL YEAR PROJECT REVIEW — PHASE I
Feasibility Analysis: Technical, Economic, Operational & Environmental
09
Department of Information Technology | Confidence-Driven Probabilistic ML & RAG Energy Planning Framework
Technical Feasibility
• Leverages proven deep learning architectures (LSTM) and gradient boosting frameworks (XGBoost, LightGBM, Random Forest).
• Residual uncertainty modeling uses robust statistical principles (standard normal critical values z_0.95, z_0.975, z_0.995).
• RAG pipeline is built using efficient FAISS vector indexing and state-of-the-art quantized LLMs (Llama-3/Mistral/Ollama).
Economic Feasibility
• Zero data acquisition costs: utilizes openly accessible public datasets from CEA, Grid-India, and NASA POWER.
• 100% open-source software stack (Python, TensorFlow, Scikit-learn, FAISS, Streamlit) eliminates proprietary licensing fees.
• Minimal computational footprint: training and inference execute seamlessly on standard workstation GPUs / multi-core CPUs.
Operational Feasibility
• Seamlessly integrates into existing SLDC and utility operational workflows via intuitive dashboard visualizations.
• Translates complex probabilistic interval math into clear, color-coded risk alerts and transparent numerical bounds.
• Maintains human-in-the-loop governance: RAG provides actionable recommendations while engineers retain final dispatch control.
Environmental Feasibility
• Facilitates maximum integration of intermittent renewable sources (solar and wind) into the state energy mix.
• Minimizes fossil-fuel spinning reserve wastage and renewable curtailment through accurate 3-month lookahead gap forecasts.
• Directly aligns with India's carbon neutrality targets and state-level renewable purchase obligations (RPO).

## Slide 10
FINAL YEAR PROJECT REVIEW — PHASE I
Resource Requirements & Risk Assessment Matrix
10
Department of Information Technology | Confidence-Driven Probabilistic ML & RAG Energy Planning Framework
SYSTEM RESOURCE REQUIREMENTS
Hardware Requirements:
• Processor: Multi-core CPU (Intel Core i5/i7/i9 or AMD Ryzen 5/7/9)
• System Memory: 16 GB DDR4/DDR5 RAM (minimum)
• Graphics Accelerator: NVIDIA GPU (CUDA-compatible) for deep learning and vector operations
• Storage: 50 GB SSD for datasets, trained model weights, and FAISS indices
Software & Development Stack:
• Operating System: Windows 11 / Linux (Ubuntu 22.04 LTS)
• Programming Runtime: Python 3.11 / Python 3.12
• ML/DL Libraries: TensorFlow/Keras, Scikit-learn, XGBoost, LightGBM
• Data & Scientific: Pandas, NumPy, SciPy, Joblib
• RAG & Vector Database: FAISS (CPU/GPU), LangChain / LlamaIndex, Ollama / HuggingFace Transformers
• Development Environment: Jupyter Notebook, VS Code / Antigravity IDE
RISK ASSESSMENT & MITIGATION MATRIX
Identified Risk | Impact | Mitigation Strategy
High Renewable Weather Volatility | High | Integrate multi-source weather data (temperature, irradiance, humidity) & multi-tier 90/95/99% prediction intervals.
Overfitting on Seasonal Peaks | Medium | Implement time-series chronological train/test split, lag features, rolling windows, and cyclical harmonic encoders.
LLM Hallucination in Planning | High | Strict RAG architecture with top-k vector retrieval from authoritative energy policies, temperature clamping & prompt constraints.
Data Inconsistency across Sources | Medium | Robust preprocessing pipeline with automated date normalization, missing-value interpolation, and unit harmonization.

## Slide 11
FINAL YEAR PROJECT REVIEW — SYSTEM ARCHITECTURE
Proposed System Overview & End-to-End Architecture
DATA INGESTION LAYER: Historical Energy Records (CEA, NITI Aayog) + Weather Data (NASA POWER, IMD)
PREPROCESSING & FEATURE ENGINEERING: Missing Value Imputation • Date Alignment • Lag (1,2,3,6,12) • Rolling Averages • Cyclical Encoders • MinMax Scaling
MODULE A: ELECTRICITY DEMAND FORECASTING
• Model: LSTM Sequence Model (Lookback = 3) • Outputs: Point Demand (D_hat) & Uncertainty (sigma_D = 391.30 MU) • Multi-Level Intervals: 90%, 95%, 99% Demand PIs
MODULE B: ELECTRICITY SUPPLY FORECASTING
• Model: LSTM Sequence Model (8 Sources, Lookback = 6) • Outputs: Point Supply (S_hat) & Uncertainty (sigma_S = 996.83 MU) • Multi-Level Intervals: 90%, 95%, 99% Supply PIs
DEMAND–SUPPLY GAP ANALYSIS & PROBABILISTIC UNCERTAINTY PROPAGATION
Gap Equation: G_hat = D_hat - S_hat | Combined Uncertainty: sigma_G = sqrt(sigma_D^2 + sigma_S^2) = 1,070.88 MU | 90%, 95%, 99% Gap Prediction Intervals Condition Classification: Shortage (G_hat > 0) • Balanced (G_hat = 0) • Surplus (G_hat < 0) | Deterministic Risk: Low (<3000) • Moderate (3000-4500) • High (>4500 MU)
RETRIEVAL-AUGMENTED GENERATION (RAG) & ENERGY PLANNING RECOMMENDATION ENGINE
• Knowledge Base: Energy Acts, TNERC Grid Codes, CEA Planning Reports, SLDC Operating Norms, Demand Response Protocols • Vector Store & Retrieval: Domain Text Chunking -> Dense Embeddings -> FAISS Vector Database (Top-k Semantic Similarity Search) • LLM Synthesis: Forecast Numbers + Risk Severity + Retrieved Regulatory Evidence -> Contextual Energy Planning Actions • Final Deliverable: Generation Scheduling, Power Trading, Peaking Plant Dispatch, Maintenance Planning & Grid Reliability Support

## Slide 12
FINAL YEAR PROJECT REVIEW — PHASE I
Methodology Flowchart & Stage-by-Stage Pipeline
12
Department of Information Technology | Confidence-Driven Probabilistic ML & RAG Energy Planning Framework
Step 1: Data Collection (CEA, NITI Aayog, NASA POWER, IMD: 129 monthly records)
Step 2: Data Preprocessing & Feature Engineering (Lags 1-12, Rolling Means, Sin/Cos)
Step 3: Independent ML Training: RF, XGBoost, LightGBM, LSTM (80/20 Chronological Split)
Step 4: Model Evaluation & Selection via MAE, RMSE, MAPE, and R² Metrics
Step 5: Point Forecasting for Demand (D_hat) and Source-Wise Generation (S_hat)
Step 6: Residual Uncertainty Quantification: sigma_D = 391.30 MU, sigma_S = 996.83 MU
Step 7: Multi-Level Prediction Intervals Generation: 90%, 95%, and 99% Bounds
Step 8: Demand–Supply Gap & Combined Uncertainty: G_hat = D_hat - S_hat, sigma_G = 1070.88 MU
Step 9: Deterministic Risk Classification (Shortage/Surplus; Low, Moderate, High Impact)
Step 10: RAG Vector Retrieval (FAISS) + LLM Synthesis -> Energy Planning Policy Actions
METHODOLOGICAL STAGES BREAKDOWN
Phase I: Data Integration & Engineering
129 monthly rows (Apr 2015 – Dec 2025). Missing values imputed. Features include 3-month and 6-month historical lookbacks, rolling statistics, and cyclical calendar harmonics.
Phase II: Decoupled ML Modeling
Four candidate architectures evaluated (RF, XGBoost, LightGBM, LSTM). Models trained separately on demand and 8 supply sources. LSTM demonstrated superior long-term dependency capture.
Phase III: Residual Uncertainty & Gap Math
Residual distributions quantify empirical standard errors (sigma_e). Symmetric prediction intervals generated using standard normal critical multipliers (z=1.645, 1.960, 2.576). Gap error propagated orthogonally.
Phase IV: RAG-Grounded Decision Support
Forecast outputs and risk levels form a structured semantic query. FAISS retrieves top-k relevant energy policy clauses. LLM generates explainable dispatch and resource planning recommendations.

## Slide 13
FINAL YEAR PROJECT REVIEW — PHASE I
Materials, Methods & Experimental Data Analysis
13
Department of Information Technology | Confidence-Driven Probabilistic ML & RAG Energy Planning Framework
DATASET SPECIFICATIONS & SOURCES
Domain / Dataset | Official Source | Records / Range
Electricity Demand | NITI Aayog / CEA | 129 Months (2015-2025)
Source-Wise Supply | NITI Aayog / CEA (8 sources) | 129 Months (2015-2025)
Temperature & Humidity | NASA POWER Portal | 129 Months (Tamil Nadu)
Rainfall & Solar Irradiance | IMD / National Water Portal | 129 Months (Aggregated)
MATHEMATICAL FORMULATIONS
• Residual Standard Error: sigma_e = sqrt( sum( (y_act - y_pred)^2 ) / (N - 1) )
• Prediction Intervals (PI): PI_(1-alpha) = [ y_hat - z_(1-alpha/2) * sigma, y_hat + z_(1-alpha/2) * sigma ]
• Critical Z-Multipliers: 90% -> z=1.645 | 95% -> z=1.960 | 99% -> z=2.576
• Combined Gap & Sigma: G_hat = D_hat - S_hat | sigma_Gap = sqrt( sigma_Demand^2 + sigma_Supply^2 )
• Deterministic Risk Bands: Low: Gap < 3000 MU | Moderate: 3000-4500 MU | High: Gap > 4500 MU
DEMAND MODEL PERFORMANCE COMPARISON
Model | MAE (MU) | RMSE (MU) | MAPE (%) | R² Score
Random Forest | 741.63 | 909.69 | 6.56% | 0.31
XGBoost | 619.18 | 724.51 | 5.56% | 0.34
LightGBM | 634.18 | 748.24 | 5.66% | 0.29
LSTM (Selected) | 368.72 | 412.93 | 3.41% | 0.78
SUPPLY MODEL PERFORMANCE COMPARISON
Model | MAE (MU) | RMSE (MU) | MAPE (%) | R² Score
Random Forest | 823.30 | 1220.90 | 6.89% | 0.31
XGBoost | 847.76 | 1215.30 | 7.13% | 0.31
LightGBM | 802.74 | 1157.40 | 6.74% | 0.38
LSTM (Selected) | 731.56 | 973.93 | 6.30% | 0.56

## Slide 14
FINAL YEAR PROJECT REVIEW — PHASE I
Experimental Validation, Project Timeline & Budget
14
Department of Information Technology | Confidence-Driven Probabilistic ML & RAG Energy Planning Framework
HOLD-OUT FUTURE VALIDATION BENCHMARK (JANUARY – MARCH 2026)
Month | Actual Dem | Pred Demand | Actual Sup | Pred Supply | Actual Gap | Pred Gap | 95% Gap PI [Lower, Upper] | Condition / Risk
Jan 2026 | 10,067.00 | 11,047.51 | 10,189.56 | 8,809.63 | -122.56 | +2,237.88 | [138.99, 4,336.77] MU | Shortage (Low Risk)
Feb 2026 | 10,125.00 | 12,308.25 | 10,405.60 | 9,229.95 | -280.60 | +3,078.30 | [979.41, 5,177.19] MU | Shortage (Moderate)
Mar 2026 | 12,233.00 | 12,594.89 | 11,247.51 | 9,574.64 | +985.49 | +3,020.25 | [921.36, 5,119.14] MU | Shortage (Moderate)
PROJECT IMPLEMENTATION TIMELINE (PHASE I & II)
Project Phase | Key Deliverables & Milestones | Duration | Status
Phase I: Initiation | Literature Survey, Dataset Collection & Cleaning | Months 1–2 | Completed
Phase I: Modeling | Model Training (RF, XGB, LGBM, LSTM) & Tuning | Months 3–4 | Completed
Phase I: Analytics | Uncertainty Quantification (90/95/99% PIs) & Gap Math | Month 5 | Completed
Phase I: Review | RAG Pipeline Prototype & IEEE Paper Preparation | Month 6 | Completed
Phase II: Deployment | Interactive Web UI, Multi-Agent RAG & Live APIs | Months 7–10 | Planned
ACADEMIC PROJECT BUDGET
Resource Category | Provisioning | Cost (INR)
Hardware / Compute | Institutional Lab | ₹ 0 (In-house)
Datasets (CEA/NASA) | Open Public Portals | ₹ 0 (Open Data)
Software Frameworks | Open-Source Python | ₹ 0 (FOSS)
Vector DB & Local LLM | FAISS / Ollama Local | ₹ 0 (Zero-cost)

## Slide 15
FINAL YEAR PROJECT REVIEW — PHASE II & FUTURE SCOPE
Phase II Implementation Plan, Future Scope & Conclusions
PLANNED PHASE II IMPLEMENTATION WORK
• Interactive Web Dashboard: Deploy a production-grade Streamlit/FastAPI web interface featuring live scenario sliders, interval toggles, and condition gauges.
• Real-Time Data Ingestion: Integrate automated live weather APIs (OpenWeather / IMD) and real-time SCADA generation data streams.
• Multi-Agent RAG Architecture: Implement multi-agent cooperative verification where specialized LLM agents debate and refine dispatch recommendations.
• Hyperparameter Optimization: Explore Bayesian optimization for deep recurrent networks and automated residual calibration across shifting seasons.
FUTURE RESEARCH DIRECTIONS
• Advanced Transformer Architectures: Investigate Temporal Fusion Transformers (TFT) and Informer models for high-resolution sub-hourly load forecasting.
• Dynamic Conformal Prediction: Implement non-parametric conformal prediction intervals to capture extreme climate anomalies without assuming normal residuals.
• Battery Energy Storage (BESS) Dispatch: Incorporate automated optimal BESS charge/discharge scheduling algorithms directly into the RAG recommendation loop.
• Inter-State Grid Power Wheeling: Extend gap analytics to regional inter-state exchange corridors and dynamic spot market pricing models.
THANK YOU!
Questions & Discussion
Confidence-Driven Probabilistic Machine Learning Framework for Electricity Demand–Supply Gap Forecasting and RAG-Based Energy Planning Department of Information Technology • Academic Year 2026–2027